| Full report for square radiant |  |
| --- | --- |
| General information |  |
| Model | Simple |  |
| Expert name | Makoed A.G. |  |
| Report date | 10.06.2009 |  |
| Real weight, ct |  |  |
| Calculated weight, ct | 0.51, 0.5154 |  |
| Spread | -0.06 ct, -13.54 % |  |
| Extra Facet Girdle / Nat | No |  |
| Extra Facet Crown | No |  |
| Extra Facet Pavilion | No |  |
| Appraiser title | AGS_2005 |  |
| Overall cut quality | N/A |  |
| Symmetry appraiser title | Internal |  |
| Overall symmetry quality | GD |  |

## Main parameters

| Width | Length | Ratio (L/W) | Corner Ratio | Diameter Minimum | Diameter Maximum | Total height | MIC |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 4.431 mm | 4.518 mm | 1.020 | 1.005 | 4.431 mm | 5.584 mm | 3.040 mm | 4.418 mm |

| Parameter |  | Avg | Min | Max | Dev | Cut | Sym |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Diameter | mm |  | 4.431 | 5.584 |  | N/A |  |
| Diameter: Corner | % | 124.69 | 124.40 | 124.98 | 0.58 |  |  |
| Diameter: Corner | mm | 5.525 | 5.512 | 5.538 | 0.026 |  |  |
| Radius | % | 55.64 | 49.85 | 63.44 | 13.59 |  |  |
| Radius | mm | 2.465 | 2.209 | 2.811 | 0.602 |  |  |
| Crown height: Side | % | 11.71 | 11.16 | 12.02 | 0.85 | N/A | VG |
| Crown height: Side | mm | 0.519 | 0.495 | 0.533 | 0.038 |  |  |
| Crown height: Joint | % | N/A | N/A | N/A | N/A |  |  |
| Crown height: Joint | mm | N/A | N/A | N/A | N/A |  |  |
| Pavilion height: Side | % | 51.57 | 50.77 | 52.32 | 1.55 | N/A | GD |
| Pavilion height: Side | mm | 2.285 | 2.250 | 2.319 | 0.069 |  |  |
| Pavilion height: Joint | % | N/A | N/A | N/A | N/A |  |  |
| Pavilion height: Joint | mm | N/A | N/A | N/A | N/A |  |  |
| Total height | % | 68.61 |  |  |  | N/A |  |
| Table: Side | % | 67.95 | 67.67 | 68.23 | 0.56 | Grading | EX |
| Table: Side | mm | 3.040 | 3.023 | 3.057 | 0.034 |  |  |
| Table: Corner w.r.t. Corner | % | 70.10 | 70.10 | 70.11 | 0.01 |  |  |
| Table: Corner w.r.t. Width | % | 87.41 | 87.20 | 87.63 | 0.43 |  |  |
| Table: Corner | mm | 3.873 | 3.864 | 3.883 | 0.019 |  |  |
| Culet | % | 0.60 | 0.37 | 0.68 | 0.30 | 0 | EX |
| Culet | mm | 0.026 | 0.017 | 0.030 | 0.013 |  |  |
| Girdle thickness: Side | % | 5.33 | 4.84 | 5.84 | 1.00 |  | GD |
| Girdle thickness: Side | mm | 0.236 | 0.215 | 0.259 | 0.044 |  |  |
| Girdle thickness: Joint | % | N/A | N/A | N/A | N/A |  | N/A |
| Girdle thickness: Joint | mm | N/A | N/A | N/A | N/A |  |  |
| Girdle facet angle | ° | 86.97 | 84.29 | 89.99 | 5.69 |  |  |
| Girdle side | % | 75.81 | 74.67 | 76.89 | 2.21 |  |  |
| Girdle side | mm | 3.359 | 3.309 | 3.407 | 0.098 |  |  |
| Girdle side corner | % | 18.11 | 17.52 | 18.86 | 1.34 |  |  |
| Girdle side corner | mm | 0.802 | 0.777 | 0.836 | 0.059 |  |  |
| Girdle internal angle | ° | 135.0 | 131.9 | 138.1 | 6.2 |  |  |
| Corner angle width | % | 12.02 | 11.71 | 12.69 | 0.98 |  |  |
| Corner angle width | mm | 0.532 | 0.519 | 0.563 | 0.043 |  |  |
| Corner angle length | % | 12.23 | 11.52 | 13.07 | 1.56 |  |  |
| Corner angle length | mm | 0.542 | 0.510 | 0.579 | 0.069 |  |  |
| Crown 1 Main angle | ° | 40.17 | 39.07 | 41.18 | 2.11 |  |  |
| Crown 1 Main height | % | 6.42 | 6.36 | 6.50 | 0.14 |  |  |
| Crown 1 Main height | mm | 0.285 | 0.282 | 0.288 | 0.006 |  |  |
| Crown 1 Corner angle | ° | 37.14 | 36.55 | 37.63 | 1.08 |  |  |
| Crown 1 Corner height | % | 6.56 | 6.11 | 6.88 | 0.78 |  |  |
| Crown 1 Corner height | mm | 0.291 | 0.271 | 0.305 | 0.034 |  |  |
| Crown 2 Main angle | ° | 33.29 | 32.97 | 33.81 | 0.83 |  |  |
| Crown 2 Main height | % | 5.56 | 5.30 | 5.77 | 0.47 |  |  |
| Crown 2 Main height | mm | 0.247 | 0.235 | 0.256 | 0.021 |  |  |
| Crown 2 Corner angle | ° | 28.62 | 28.38 | 28.82 | 0.44 |  |  |
| Crown 2 Corner height | % | 5.48 | 5.33 | 5.61 | 0.28 |  |  |
| Crown 2 Corner height | mm | 0.243 | 0.236 | 0.249 | 0.012 |  |  |

| Parameter |  | Avg | Min | Max | Dev |
| --- | --- | --- | --- | --- | --- |
| Crown Star angle | ° | 24.09 | 22.97 | 24.72 | 1.75 |
| Crown Star height | % | 5.12 | 4.73 | 5.40 | 0.68 |
| Crown Star height | mm | 0.227 | 0.209 | 0.239 | 0.030 |
| Pavilion 1 Main angle | ° | 67.12 | 58.91 | 70.42 | 11.51 |
| Pavilion 1 Main height | % | 18.90 | 17.87 | 19.49 | 1.63 |
| Pavilion 1 Main height | mm | 0.837 | 0.792 | 0.864 | 0.072 |
| Pavilion 1 Corner angle | ° | 44.72 | 44.05 | 45.18 | 1.13 |
| Pavilion 1 Corner height | % | 9.27 | 8.56 | 10.00 | 1.44 |
| Pavilion 1 Corner height | mm | 0.411 | 0.379 | 0.443 | 0.064 |
| Pavilion 2 Main angle | ° | N/A | N/A | N/A | N/A |
| Pavilion 2 Main height | % | N/A | N/A | N/A | N/A |
| Pavilion 2 Main height | mm | N/A | N/A | N/A | N/A |
| Pavilion 2 Corner angle | ° | 38.89 | 37.93 | 39.51 | 1.58 |
| Pavilion 2 Corner height | % | 42.27 | 41.02 | 43.16 | 2.14 |
| Pavilion 2 Corner height | mm | 1.873 | 1.818 | 1.913 | 0.095 |
| Pavilion Halves 1 angle | ° | 40.05 | 39.23 | 40.64 | 1.41 |
| Pavilion Halves 1 height | % | 47.16 | 46.05 | 48.33 | 2.28 |
| Pavilion Halves 1 height | mm | 2.090 | 2.040 | 2.141 | 0.101 |
| Pavilion Halves 2 angle | ° | 41.04 | 39.65 | 42.91 | 3.26 |
| Pavilion Halves 2 height | % | 47.13 | 46.02 | 48.39 | 2.37 |
| Pavilion Halves 2 height | mm | 2.088 | 2.039 | 2.144 | 0.105 |
| Pavilion Halves 3 angle | ° | 41.06 | 39.73 | 43.31 | 3.57 |
| Pavilion Halves 3 height | % | 34.54 | 33.01 | 35.63 | 2.62 |
| Pavilion Halves 3 height | mm | 1.531 | 1.463 | 1.579 | 0.116 |

## Detailed parameters

| Parameter |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Diameter: Corner | % | 124.40 | 124.98 |  |  |  |  |  |  |
| Diameter: Corner | mm | 5.512 | 5.538 |  |  |  |  |  |  |
| Crown height: Side | % | 12.02 | 11.96 | 11.88 | 11.77 | 11.45 | 11.16 | 11.57 | 11.90 |
| Crown height: Side | mm | 0.533 | 0.530 | 0.527 | 0.522 | 0.507 | 0.495 | 0.512 | 0.527 |
| Crown height: Joint | % | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A |
| Crown height: Joint | mm | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A |
| Pavilion height: Side | % | 50.77 | 51.39 | 51.48 | 51.52 | 52.32 | 52.28 | 51.92 | 50.87 |
| Pavilion height: Side | mm | 2.250 | 2.277 | 2.281 | 2.283 | 2.319 | 2.317 | 2.301 | 2.254 |
| Pavilion height: Joint | % | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A |
| Pavilion height: Joint | mm | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A |
| Table: Side | % | 68.23 | 67.67 |  |  |  |  |  |  |
| Table: Side | mm | 3.023 | 3.057 |  |  |  |  |  |  |
| Table: Corner w.r.t. Corner | % | 70.10 | 70.11 |  |  |  |  |  |  |
| Table: Corner w.r.t. Width | % | 87.20 | 87.63 |  |  |  |  |  |  |
| Table: Corner | mm | 3.864 | 3.883 |  |  |  |  |  |  |
| Girdle thickness: Side | % | 5.83 | 5.26 | 5.25 | 5.33 | 4.84 | 5.17 | 5.13 | 5.84 |
| Girdle thickness: Side | mm | 0.258 | 0.233 | 0.233 | 0.236 | 0.215 | 0.229 | 0.227 | 0.259 |
| Girdle thickness: Joint | % | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A |
| Girdle thickness: Joint | mm | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A |
| Girdle facet angle | ° | 88.69 | 86.36 | 84.68 | 87.23 | 84.75 | 89.74 | 89.99 | 84.29 |
| Girdle facet azimuth | ° | 359.6 | 44.3 | 89.0 | 133.6 | 180.0 | 221.9 | 269.9 | 315.0 |
| Corner angle width | % | 11.89 | 11.76 | 11.71 | 12.69 |  |  |  |  |
| Corner angle width | mm | 0.527 | 0.521 | 0.519 | 0.563 |  |  |  |  |
| Corner angle length | % | 11.68 | 11.52 | 13.07 | 12.66 |  |  |  |  |
| Corner angle length | mm | 0.518 | 0.510 | 0.579 | 0.561 |  |  |  |  |
| Crown 1 Main angle | ° | 40.27 | 41.18 | 40.18 | 39.07 |  |  |  |  |
| Crown 1 Main height | % | 6.50 | 6.44 | 6.36 | 6.38 |  |  |  |  |
| Crown 1 Main height | mm | 0.288 | 0.286 | 0.282 | 0.283 |  |  |  |  |
| Crown 1 Main azimuth | ° | 359.9 | 89.0 | 179.9 | 270.7 |  |  |  |  |
| Crown 1 Corner angle | ° | 37.42 | 37.63 | 36.97 | 36.55 |  |  |  |  |
| Crown 1 Corner height | % | 6.80 | 6.88 | 6.11 | 6.46 |  |  |  |  |
| Crown 1 Corner height | mm | 0.301 | 0.305 | 0.271 | 0.286 |  |  |  |  |
| Crown 1 Corner azimuth | ° | 42.5 | 132.1 | 220.5 | 314.3 |  |  |  |  |
| Crown 2 Main angle | ° | 33.21 | 33.18 | 33.81 | 32.97 |  |  |  |  |
| Crown 2 Main height | % | 5.77 | 5.56 | 5.30 | 5.63 |  |  |  |  |
| Crown 2 Main height | mm | 0.256 | 0.246 | 0.235 | 0.250 |  |  |  |  |
| Crown 2 Main azimuth | ° | 359.9 | 89.1 | 179.8 | 270.7 |  |  |  |  |
| Crown 2 Corner angle | ° | 28.38 | 28.82 | 28.58 | 28.68 |  |  |  |  |
| Crown 2 Corner height | % | 5.55 | 5.43 | 5.33 | 5.61 |  |  |  |  |
| Crown 2 Corner height | mm | 0.246 | 0.241 | 0.236 | 0.249 |  |  |  |  |
| Crown 2 Corner azimuth | ° | 42.1 | 131.2 | 220.3 | 314.5 |  |  |  |  |

| Parameter |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Crown Star angle | ° | 24.57 | 23.79 | 24.72 | 24.02 | 24.18 | 22.97 | 24.01 | 24.49 |
| Crown Star height | % | 5.20 | 5.27 | 4.96 | 5.07 | 4.93 | 4.73 | 5.40 | 5.40 |
| Crown Star height | mm | 0.230 | 0.233 | 0.220 | 0.225 | 0.219 | 0.209 | 0.239 | 0.239 |
| Crown Star azimuth | ° | 5.7 | 82.7 | 94.7 | 173.5 | 186.2 | 264.1 | 277.3 | 353.8 |
| Pavilion 1 Main angle | ° | 70.42 | 69.01 | 58.91 | 70.13 |  |  |  |  |
| Pavilion 1 Main height | % | 19.27 | 17.87 | 18.96 | 19.49 |  |  |  |  |
| Pavilion 1 Main height | mm | 0.854 | 0.792 | 0.840 | 0.864 |  |  |  |  |
| Pavilion 1 Main azimuth | ° | 359.8 | 89.0 | 180.3 | 269.6 |  |  |  |  |
| Pavilion 1 Corner angle | ° | 44.99 | 45.18 | 44.64 | 44.05 |  |  |  |  |
| Pavilion 1 Corner height | % | 9.10 | 8.56 | 9.40 | 10.00 |  |  |  |  |
| Pavilion 1 Corner height | mm | 0.403 | 0.379 | 0.417 | 0.443 |  |  |  |  |
| Pavilion 1 Corner azimuth | ° | 46.3 | 134.5 | 223.8 | 314.2 |  |  |  |  |
| Pavilion 2 Main angle | ° | N/A | N/A | N/A | N/A |  |  |  |  |
| Pavilion 2 Main height | % | N/A | N/A | N/A | N/A |  |  |  |  |
| Pavilion 2 Main height | mm | N/A | N/A | N/A | N/A |  |  |  |  |
| Pavilion 2 Main azimuth | ° | N/A | N/A | N/A | N/A |  |  |  |  |
| Pavilion 2 Corner angle | ° | 38.82 | 37.93 | 39.31 | 39.51 |  |  |  |  |
| Pavilion 2 Corner height | % | 42.58 | 42.33 | 43.16 | 41.02 |  |  |  |  |
| Pavilion 2 Corner height | mm | 1.887 | 1.876 | 1.913 | 1.818 |  |  |  |  |
| Pavilion 2 Corner azimuth | ° | 45.0 | 135.2 | 224.8 | 315.1 |  |  |  |  |
| Pavilion Halves 1 angle | ° | 39.85 | 40.14 | 39.23 | 39.68 | 40.64 | 40.23 | 40.36 | 40.30 |
| Pavilion Halves 1 height | % | 47.05 | 46.67 | 47.46 | 47.62 | 48.33 | 47.77 | 46.05 | 46.32 |
| Pavilion Halves 1 height | mm | 2.085 | 2.068 | 2.103 | 2.110 | 2.141 | 2.117 | 2.040 | 2.052 |
| Pavilion Halves 1 azimuth | ° | 34.8 | 58.5 | 121.5 | 149.4 | 210.9 | 233.6 | 305.3 | 323.1 |
| Pavilion Halves 2 angle | ° | 40.49 | 40.65 | 39.65 | 42.34 | 42.91 | 40.77 | 40.71 | 40.84 |
| Pavilion Halves 2 height | % | 46.38 | 47.46 | 47.24 | 47.06 | 48.39 | 47.89 | 46.02 | 46.61 |
| Pavilion Halves 2 height | mm | 2.055 | 2.103 | 2.093 | 2.085 | 2.144 | 2.122 | 2.039 | 2.065 |
| Pavilion Halves 2 azimuth | ° | 28.2 | 63.6 | 117.1 | 164.4 | 196.4 | 240.2 | 299.8 | 330.4 |
| Pavilion Halves 3 angle | ° | 40.32 | 40.43 | 39.73 | 43.02 | 43.31 | 40.65 | 40.31 | 40.68 |
| Pavilion Halves 3 height | % | 33.01 | 35.13 | 35.63 | 34.28 | 33.91 | 35.59 | 34.08 | 34.71 |
| Pavilion Halves 3 height | mm | 1.463 | 1.557 | 1.579 | 1.519 | 1.502 | 1.577 | 1.510 | 1.538 |
| Pavilion Halves 3 azimuth | ° | 19.2 | 70.4 | 107.8 | 171.1 | 188.7 | 249.3 | 286.8 | 338.9 |
| Girdle side | % | 75.91 | 75.77 | 76.89 | 74.67 |  |  |  |  |
| Girdle side | mm | 3.364 | 3.357 | 3.407 | 3.309 |  |  |  |  |
| Girdle side corner | % | 17.52 | 17.82 | 18.23 | 18.86 |  |  |  |  |
| Girdle side corner | mm | 0.777 | 0.790 | 0.808 | 0.836 |  |  |  |  |
| Girdle internal angle | ° | 135.3 | 135.3 | 135.4 | 133.6 | 138.1 | 131.9 | 135.0 | 135.3 |
| Girdle internal angle deviation from average | ° | 0.3 | 0.3 | 0.4 | -1.4 | 3.1 | -3.1 | -0.0 | 0.3 |

| Offset |  | Distance | Width wise | Length wise |
| --- | --- | --- | --- | --- |
| Culet-Table offset by table axis | % | 1.89 ± 0.30 | 1.74 | 0.73 |
| Culet-Table offset by table axis | mm | 0.084 ± 0.013 | 0.077 | 0.032 |
| Girdle-Culet offset by table axis | % | 1.04 ± 0.29 | 0.58 | 0.87 |
| Girdle-Culet offset by table axis | mm | 0.046 ± 0.013 | 0.026 | 0.039 |
| Girdle-Table offset by table axis | % | 1.17 ± 0.25 | 1.16 | 0.14 |
| Girdle-Table offset by table axis | mm | 0.052 ± 0.011 | 0.052 | 0.006 |
| Girdle to table-culet line offset | % | 0.85 |  |  |
| Girdle to table-culet line offset | mm | 0.037 |  |  |

| Culet shift ratio by width & length |  |
| --- | --- |
| Width | 4.431 mm, 100% |
| Width-wise culet shift ratio | 2.258 mm, 50.95 % | 2.174 mm, 49.05 % |
| Length-wise culet shift ratio | 2.214 mm, 49.96 % | 2.308 mm, 52.09 % |
| Length | 4.518 mm, 100% |
| Length-wise culet shift ratio | 2.214 mm, 49.00 % | 2.308 mm, 51.09 % |

## Crown and pavilion views of the diamond with indication of Width & Length

Invisible edges are hidden

Invisible edges are drawn taking refraction into account

## Plots

Girdle thickness plot

Diameter variation plot

## Girdle asymmetry

| Girdle asymmetry | Recommendation for girdle asymmetry removing |
| --- | --- |

## Facets slope and azimuth angles

Pavilion and crown views of the diamond with indication of main facets slope angles Invisible edges are drawn taking refraction into account

Pavilion and crown views of the diamond with indication of facets slope angles

Pavilion and crown views of the diamond with indication of facets azimuth angles

## Girdle facets slope and azimuth angles

Pavilion and crown views of the diamond with indication of girdle facets slope angles

Pavilion and crown views of the diamond with indication of deviation of girdle facets slope angles from there ideal (90°)

Pavilion and crown views of the diamond with indication of girdle facets azimuth angles

Pavilion and crown views of the diamond with indication of deviation of girdle facets azimuth angles

## Facets heights

Pavilion and crown views of the diamond with indication of facets heights (mm)

Pavilion and crown views of the diamond with indication of facets heights (%)

Pavilion and crown views of the diamond with indication of deviation of facets heights from the average values (mm)

Pavilion and crown views of the diamond with indication of deviation of facets heights from the average values (%)

## Pavilion and Crown heights: Side

Pavilion and Crown heights: Side (mm)

Pavilion and Crown heights: Side (%)

Deviations of Pavilion and Crown heights: Side from the average values (mm)

Deviations of Pavilion and Crown heights: Side from the average values (%)

## Additional Illustrations

Pavilion and crown views of the diamond with indication of the maximum circle that may be inscribed (MIC) in the girdle outline along with the section of the model in the circle's plane

Pavilion and crown views of the diamond with indication of invisible edges without refraction

|  | Girdle center |  | Culet center |  | Тable center |  | MIC center |
| --- | --- | --- | --- | --- | --- | --- | --- |